## Slide 1
UTF-8 validation without processor lock-in
Two Parabix expressions · exact-boundary correctness · performance study [Team member names] · August 5, 2026
CMPT 980 · SIMD Application Study
Notes: Open with the compiler question: can target-independent abstractions preserve the value of a hand-tuned SIMD algorithm?
[Sources]
- Project repository: https://github.com/Grendlee/GrantPrit

## Slide 2
2
UTF-8 is locally encoded—but globally stateful
ASCII
00–7F stands alone. It is the fast path for most English text.
Continuation
80–BF is legal only where a prior leader created scope.
Leaders
C2–DF, E0–EF, and F0–F4 require one, two, or three following bytes.
Narrow ranges
E0, ED, F0, and F4 constrain byte two to prevent overlong, surrogate, or out-of-range values.
Notes: Explain that vector lanes do not remove dependencies: leaders create required positions that can cross blocks and EOF.
[Sources]
- Unicode Standard Chapter 3, Table 3-7: https://www.unicode.org/versions/latest/ch03.pdf

## Slide 3
3
Three implementations isolate the compiler trade-off
DIRECT IDISA Packed byte lanes comparisons · dslli · XOR · popcount
PABLO / u8u16 Basis bit streams character classes · Advance · AtEOF
KEISER–LEMIRE Native SIMD vectors lookup/shuffle-oriented hand-written code
Notes: The scalar decoder is an oracle, not the main SIMD comparison. The two Parabix paths differ in representation and compiler work.
[Sources]
- Keiser & Lemire: https://arxiv.org/abs/2010.03090; repository: https://github.com/Grendlee/GrantPrit

## Slide 4
4
The same UTF-8 rule becomes two compiler-facing programs
Direct bytes
Keep the previous vector block. Align bytes at distances 1/2/3. XOR expected continuation lanes with actual 80–BF lanes. Add narrow range masks. Reduce error lanes.
Pablo scopes
Transpose bytes into eight basis streams. Compile byte classes. Advance leaders into scope22/32/33/42/43/44. XOR scope with suffixes. Mark outstanding scope at EOF.
Notes: Emphasize what the compiler sees: generic lane operations in the direct path versus boolean stream algebra in Pablo.
[Sources]
- Update2Work/utf8_validation_kernel.cpp and Update2Work/utf8_pablo_validation_kernel.cpp

## Slide 5
5
Exact block boundaries exposed a real correctness gap
Original behavior
… 41 41 E2 | EOF A partial block supplied zeros and often exposed missing suffixes. At an exact multiple, no following padded block was guaranteed. The unfinished leader could be accepted.
Completed behavior
Keep direct state across blocks. Add a direct-byte EOF guard. Count Add1 error streams correctly. AtEOF(outstanding scope) makes termination part of validation.
Notes: Show why ordinary short truncated tests were insufficient. Exact B, 2B, and 3B lengths are distinct semantic cases.
[Sources]
- Professor feedback supplied by the user; reproduced by Update2Work/tests/run_utf8_validation_tests.py

## Slide 6
Both compiler-generated validators agree with the oracle
124 generated cases per width · malformed ranges · crossing sequences · B±3 · exact B/2B/3B truncation
Oracle / implementation
64-bit
128-bit
256-bit
512-bit
Overall
Python strict UTF-8
124/124
124/124
124/124
124/124
496/496
Direct IDISA + EOF guard
124/124
124/124
124/124
124/124
496/496
Pablo validation-only
124/124
124/124
124/124
124/124
496/496
496 / 496 cases passed
Direct · Pablo · independent strict decoder
6
Notes: Report the result precisely. Agreement is across four configured SIMD widths, not just the machine default.
[Sources]
- Update2Work/tests/run_utf8_validation_tests.py; verified run on August 3, 2026

## Slide 7
7
Performance evidence is the remaining group checkpoint
measured trials after warmup
median throughput and variability
threads, capped at physical cores
10+
1 · 2 · 4 · 8
GB/s + IQR
Do not fill this slide with invented throughput
The groupmate must insert the verified single-thread chart and 1/2/4/8-thread scaling chart from raw CSV before submission.
Notes: Groupmate owns the measurements and plots. Separate JIT/setup and file I/O from steady-state validation; validate outputs before accepting timings.
[Sources]
- Update2Work/BENCHMARK_HANDOFF.md

## Slide 8
EOF belongs in the algorithm
Portable SIMD works.
Boundaries are semantic.
Next: benchmark codegen.
WHAT WE LEARNED
Notes: Close by resolving the opening question: the abstractions are expressive and correct; the benchmark will determine their performance cost relative to hand-written SIMD.
[Sources]
- Verified project implementation and test suite